Miniguide US Remote Unit

Quick Start

# This unit is an accessory for the Miniguide US.
1-07006-00 Miniguide US w/ Print User’s Guide

1-07007-00 Miniguide US w/ Braille User’s Guide

Plug Remote Unit’s cable into jack located in back of Miniguide US. Remote Unit mimics the vibration patterns—speed and duration—of the Miniguide US. When Orientation and Mobility Instructors hold the Remote, they feel exactly what their students feel; and therefore they can provide more accurate Miniguide US instruction.

Remote Unit uses 1 AAA Alkaline battery, which is provided. To install battery, hold Remote with button facing down and away from you.  Place small flat object such as a dime or small screw driver in slot just above cable attachment point. Pull up and lift off back half of Remote case. Battery cradle is partially covered on both ends. Place flat, negative end of battery in middle of cradle with positive, pointed end angled toward you. Move battery forward until negative end fits firmly into far end of cradle and positive end slides into near end of cradle. Positive end of cradle is marked by a plus sign and negative end by a minus sign. The battery fits into the cradle very tightly. When removing the battery, you may need to use a dime or small screw to pop it out.

PARTS LIST Page 2 of 2

Miniguide US Remote Unit Catalog Number 1-07009-00 APH Number Item Description Quantity Remote Unit – Miniguide US 1 Alkaline Battery, AAA-size 1 Remote Unit Manual, Print 1 Remote Unit Manual, Embossed 1 Remote Unit Manual, on CD 1 Quick Start Sheet / Parts List, Print 1 Quick Start Sheet / Parts List, Embossed 1

APH Number items may be purchased separately

AMERICAN PRINTING HOUSE FOR THE BLIND P.O. BOX 6085, LOUISVILLE, KY 40206-0085 OpEngr110119